## Slide 1: MIPS Simulator
Yong LI
2019/07/31

## Slide 2: Agenda
Background
  Assumptions
  Naming convention
  Instruction implemented
Main Components
  Memory, Registers
  Pipeline 5 stages
  4 Latches
  User Interfaces
Data Flow
Hazard handling
  Data Hazard
  Control Hazard

## Slide 3: Assumptions
All instructions take 5 stages, no more no less
Reg writes completed at the 1st half cycle
Reg read completed at the 2nd half cycle
No forwarding, No interrupts, No branch prediction

## Slide 4: Naming Convention
Clock starts from 1.
Stage + Clock:
  ID2 : stage ID at Clock 2
  EX3: stage EX at Clock 3
 | IF | ID | EX | MEM | WB |  | 
1 | IF1 |  |  |  |  |  | inst 1
2 | IF2 | ID2 |  |  |  |  | inst 2
3 |  | ID3 | EX3 |  |  |  | 
4 |  |  | EX4 | MEM4 |  |  | 
5 |  |  |  | MEM5 | WB5 |  | 
6 |  |  |  |  | WB6 |  | 

## Slide 5: Instructions
 | ASM | Type | Type | Inst | Code
1 | beq $s, $t, offset | branch | I | beq | if $s == $t advance_pc (offset << 2)); else advance_pc (4);
2 | lw $t, offset($s) | load/store | I | lw | $t = MEM[$s + offset]; advance_pc (4);
3 | sw $t, offset($s) | load/store | I | sw | MEM[$s + offset] = $t; advance_pc (4);
4 | addi $t, $s, imm | alu_ri | I | addi | $t = $s + imm; advance_pc (4);
5 | andi $t, $s, imm | alu_ri | I | andi | $t = $s & imm; advance_pc (4);
6 | lui $t, imm | alu_ri | I | lui | $t = (imm << 16); advance_pc (4);
7 | ori $t, $s, imm | alu_ri | I | ori | $t = $s ¦ imm; advance_pc (4);
8 | slti $t, $s, imm | alu_ri | I | slti | if $s < imm $t = 1; advance_pc (4); else $t = 0; advance_pc (4);
9 | sltiu $t, $s, imm | alu_ri | I | sltiu | if $s < imm $t = 1; advance_pc (4); else $t = 0; advance_pc (4);
10 | add $d, $s, $t | alu_rr | R | add | $d = $s + $t; advance_pc (4);
11 | and $d, $s, $t | alu_rr | R | and | $d = $s & $t; advance_pc (4);
12 | mul $d,$s,$t, | alu_rr | R | mul | $(d+1) = (uint32) MSB(s*t), $d = (uint32) LSB(s*t)
13 | or $d, $s, $t | alu_rr | R | or | $d = $s ¦ $t; advance_pc (4);
14 | sll $d, $t, h | alu_rr | R | sll | $d = $t << h; advance_pc (4);
15 | srl $d, $t, h | alu_rr | R | srl | $d = $t >> h; advance_pc (4);
16 | sub $d, $s, $t | alu_rr | R | sub | $d = $s - $t; advance_pc (4);
16 totally
4 Categories
Branch
Load/Store
ALU-Reg-Imm
ALU-Reg-Reg
MUL function is different than standard MUL

## Slide 6: Memory
- Address starts from 0
- 2048 Bytes.
  uint8_t mem[2048]
- Addresses [0,4,8,12...2044]
- Instruction Mem/Data Mem

## Slide 7: Stage Sequence
IF
ID
EX
MEM
WB
https://en.wikipedia.org/wiki/MIPS_architecture_processors
Notes: All 5 stages are run simultaneously. ID cannot read what IF write at the same cycle, ID reads the last cycle IF output.
IF writes to new IFID_n, while ID read the IFID (old one), after ID stage, we update IFID to IFID_n.

## Slide 8: Latches and UI

## Slide 9: Input/output
Input:
  Instruction as a text file
  User directives:
    instruction/cycle mode
    number of instructions/cycles to be executed
    dump register/latch/statistic/inst memory/data memory
Output: At each clock cycle, or each instruction end, we can review:
  32 Register contents
  4 Latches register values
  Simulator performance Statistic :
    Utilization of each stage. UsefulworkCycle/CpuCycle
    Total time in CPU cycle

## Slide 10: HAZARD
Structural Hazard: Execution unit (Memory) is busy.
Solution: Duplicate resource. Separate Data Memory and Instruction Memory.
Data Hazard: Instructor i read stale register data before it is being write.
Solution:
  WAR/WAW : N/A. Only exist in Variable length pipeline.
  RAW: lock registers to be wrote. STALL pipeline when following inst read the locked reg.
Control Hazard: The inst right after branch inst may should not be executed.
Solution: Detect branch inst, then STALL the pipeline until inst jump.

## Slide 11: Data Hazard -- RAW
Controlled by checking whether the REG to be read is locked or not
Control signal: hazard_data_raw_cnt
At ID :
  Lock REGs to be wrote
  If ( IF.inst.Reg == locked) { hazard_data_raw_cnt++} else {hazard_data_raw_cnt--}
At EX:
  unlocked REGs to be write

## Slide 12: Data Hazard Example
# addi $t0, $t2, 0xe <<< $t0 will be written. $t0 get locked at ID2, unlocked at EX3.
# sub $s0, $t0, $t3 <<< STALL until IF4
# addi $t7, $zero, 0x7 <<< Start at IF5

## Slide 14: Control Hazard: BEQ
IF check the control signal (hazard_ctrl_cnt)
  If BEQ is set, then IF
    1. stop fetching
    2.set NOOP as the next inst
Detected at ID stage.,
  If op=BEQ:
    hazard_ctrl_cnt++
    IFID.inst = NOOP, pc = ppc (previous pc)
Cleared at EX stage
  If op=BEQ hazard_ctrl_cnt--

## Slide 15: BEQ Branch
If Branch Condition EXMEM.cond is set,
  IF set PC to position instructed by branch
  Then seq executing instructions from that address
Control signal: hazard_ctrl_cnt
  Cleared at EX stage after condition is true and Jump Address is calculated by ALU.

## Slide 16: BEQ Example
beq $s0, $t0, 0x2. PC0 <<< s0==t0, jump 2 instructions.
addi $t0, $zero, 0x0 . PC4 <<< skipped
addi $t1, $zero, 0x1 PC8 <<< skipped
addi $t2, $zero, 0x2 PC12 <<< jump to execute
addi $t3, $zero, 0x3 PC16 <<< continue

## Slide 17: Improvements
Improve performance by:
  Data Forwarding
  Branch prediction
  Variable instruction stage length

## Slide 18: DEMO

## Slide 19: Back up Slides

## Slide 20: TC1. REG and Latch
# addi $t0, $t2, 0xe
00100001010010000000000000001110

## Slide 21: TC1, Inst being worked on each Stage/Clock
# addi $t0, $t2, 0xe
00100001010010000000000000001110

## Slide 22: TC2. RAW. Demo
00100001010010000000000000001110 # addi $t0, $t2, 0xe
00000001000010111000000000100010 # sub $s0, $t0, $t3